## Slide 1: Configuring Route-Based IPSEC on OPNSESE
Ping from R1 to R2 on the WAN interfaces, do you have a reply? If not, fix the problem
On both routers, allow IPSEC traffic on the WAN interfaces (UDP 500, UDP 4500, ESP)
Create Pre-shared Keys with same key on both R1 and R2
On R1, go to VPN, IPSEC, connections and create a new connection (do the same on R2) and make the PSK and Children
On R1create VTI address of 10.50.50.1 and do the same on R2 with VTI address 10.50.50.2
Check if the IPSEC has been formed.
Ping from VTI of R1 to VTI on R2, is it working? If not solve the problem.
Go the HQ device and enable DHCP client, same on Branch device. Can they ping each other?
On R1, make a static route with destination 192.168.60.0/24 having gateway 10.50.50.2 (same on R2)
Ping from the LAN1 device behind R1 to LAN2 device behind R2 and vice versa

## Slide 2: Configuring Policy-Based IPSEC on OPNSENSE
Create Pre-shared Keys with same key on both R1 and R2
On R1, go to VPN, IPSEC, connections and create a new connection (do the same on R2) and make the PSK and Children
Check if the IPSEC has been formed.
Ping from the LAN1 device behind R1 to LAN2 device behind R2 and vice versa

## Slide 3: Configuring IPsec VPN with Overlapping LAN Networks (Virtual Network & 1:1 NAT)
Check what IPs are received on both end devices
Change the Child on R1 to have local Net 10.10.10.0/24 and remote 10.20.20.0/24, then do the opposite on R2
On RI go IPSEC, Security Policy Database and add a Manual entry with source 192.168.50.0/24 and destination 10.20.20.0/24. Do the same on R2 with destination 10.10.10.0/24
On R1 create a BINAT with external network 10.10.10.0/24 and source 192.168.50.0/24 and destination 10.20.20.0/24. Do the same on R2 with the right IPs
Try to ping from LAB B to LAN A on the IP 10.10.10.100, do you have a reply? Do a traceroute too
While the ping is open, make SSH to R2 and do this command: tcpdump -ni enc0 – what do you recognize (keep it on)
Switch off the VPN on R2, do you still have the ping working? Re-enable it again, is the ping working?
Do Telnet from LAN B device to LAN A device, can you reach it?

## Slide 4: Configuring remote access OpenVPN server using certificates
Go to system, trust, authorities and create a new certificate authority
From same place go to certificate & create a certificate for the server putting the type as Server Certificate and issuer the CA already created
From system, go to Users and create a new user then search certificates by username and create a new certificate as client certificate with the right CA as issuer, then check if this has been created under Certificates
Go the VPN then OpenVPN, create an instance, then static keys and create one
Create now an instance with roles as server, port UDP 1194, type TUN, with server IPv4 of 192.168.57.0/24, and choose certificate of OpenVPN server, and check verify remote certificate, certificate depth One, and the right TLS static key, local database for authentication, local network 192.168.50.0/24, option client-to-client, and push block-outside-dns, push register-dns, register dns check and DNS server 1.1.1.1 then save
Go to interfaces then assignment and add the OVPN interface and enable it.
Go to firewall, then rules, and on WAN allow UDP port 1194 on the WAN address
From the firewall ad rules, go to the OVPN interface and create a rule to pass everything to source the OVPN network
Export the client OVPN config as file only with hostname x.x.x.x

## Slide 5: Configuring remote access OpenVPN client using certificates
Download and install on your PC OpenVPN connect software
Go to the downloaded OVPN file and double click on it then import it and put the right username and password
Ping to 192.168.50.100 from your PC, is it working?

## Slide 6: OPNVPN user with 2fa
Go to system, access then servers and create a new one with type local + Timebased one Time password and give it a description then save
Go to the user Maher and click on the OTP seed and scan the QR code by google authenticator
To test if this is working, go to Test under system, access, and put the username of Maher and password the google authenticator code followed by the password
Go to OpenVPN, instances, and on the authentication let the OTP then save
Check if you are going to the internet via the OpenVPN