## Slide 1: Connecting to the UniFi router
Connect to the UniFi router as shown in the picture
Download and install WiFiMan on your PC and check what IP has the UniFi router
Login to the router from the browser and follow the steps one after the other

## Slide 2: Connecting to the UniFi Switch
Connect to the UniFi switch as shown in the picture
Check from the WiFiman the IP address of the switch and try to go to that IP from the browser – is it work?
Go to the UniFi Controller (from the cloud) and check if the switch is shown there
Adopt the switch to the UniFi Controller
Check if your PC is able to go to the Internet

## Slide 3: Adopt the UniFi AP to the Controller
Login into the controller go to Devices and adopt the UniFi AP
Does it show connected?

## Slide 4: UniFi AP Configuration
Change its name to AP1
Go to settings then WiFi and create a new WiFi with a name of UniFi and password 123456789
Go to your phone and connect to the UniFi SSID. Is your phone connected to the internet?
Check from the controller if your phone is connected to the wireless

## Slide 5: Adopting and configuring AP2
Connect the 2nd AP to the switch as shown in the picture
Check if the 2nd UniFi AP has received an IP
Adopt the 2nd AP to the site
Create a new Wireless network with a name of UniFi2 and password 987654321
Check that both AP’s can work on 2 GHz and 5 GHz
Check from your phone, do you see both SSID’s?
Connect to each one of them, do you have internet?

## Slide 6: Configuring VLANs on the router
From the UCG Ultra, create VLAN10 network with VLAN ID 10 having a subnet of 10.10.10.0/24
From the UCG Ultra, create VLAN20 network with VLAN ID 20 having a subnet of 10.20.20.0/24
Go to port1 of the UCG Ultra router and leave Native VLAN to be the default one and customer to let VLAN10 and VLAN20 to pass

## Slide 7: Configuring VLANs on the switch
From the switch, go to port1 and put native vlan the default one and then the tagged VLAN to be VLAN10 and VLAN20
Do the same on port 3 (connected to AP1) and port 4 (connected to AP2)

## Slide 8: Configuring VLANs on the UniFi AP
Go to the controller then WiFi and adjust the name UniFi to Work, same password and put it on VLAN 10
Go to the controller then wireless network and adjust the name UniFi2 to Guest, same password and put it on VLAN 20
Connect the phone to the SSID Work. Do you have internet? What IP did it receive?
Connect the phone to the SSID Guest. Do you have internet? What IP did it receive?

## Slide 9: UniFi AP Band Steering
From the controller go to settings then network and enable Band Steering on AP1 and AP2

## Slide 10: Unifi Wireless Mesh
Remove AP2 from the controller
Enable Mesh Parent under AP1 on the controller
Connect AP2 to the power only
Check if AP2 has been discovered on the controller via wireless
Adopt AP2 to the controller and add the Normal SSID VLAN to AP2 only
Connect your phone to Normal SSID. Do you have internet?

## Slide 11: Unifi Innerspace
From the controller, go to the site manager and install InnerSpace
Add a new floor plan
Make the right scale
Place the adopted devices in the right place
Check the coverage on both 2GHz and 5GHz. Are the AP’s enough to cover the whole floor plan?

## Slide 12: Hide WiFi name and client isolation
From the controller, hide the Normal SSID and check if it is still shown on your phone
Try to connect to it on your phone, is it working?
On the Guest WiFi, enable client isolation

## Slide 13: Teleport VPN
Check from the control panel if remote access is enabled
Go to VPN , enable Teleport and make an invitation
From your phone, download WiFiMan app and paste the link invitation to it
Connect to the VPN, is it working?

## Slide 14: MAC Filtering & WiFi Blackout Schedule
Go to Normal WiFi and just add your phone in the MAC Filtering to be allowed
Test if your PC can connect to the Normal WiFi
Enable WiFi Blackout so only during working days from 8am to 5pm the Normal WiFi is working

## Slide 15: Hotspot with Simple password
Go to Network then VLAN 20 and enable hotspot on it
Apply the hotspot on Guest WiFi
Create a simple password for the portal and login to the Guest SSID. Are you connected to the internet?

## Slide 16: Hotspot with vouchers
Go to the landing page and on Authentication Methods uncheck password and check vouchers
Create 10 new vouchers with 2M/2M as speed and unlimited as quota
Check if you can print the vouchers
From your phone, connect to Guest SSID and use one of the vouchers and check if it works and you get to the limited speed

## Slide 17: Hotspot with Payment
Go to the landing page and on Authentication Methods uncheck Voucher and check Payment
Select a payment gateway (Stripe), put the API key with free trial for 30 min per day with 1GB, and make a new payment package on your choice.
From your phone, connect to Guest SSID and check if the page load correctly, then connect on the Free trial.