## Slide 1: Recursive DNS (unbound) on OPNsense
The OPNsense has been reset to default. Check if your computer has access to the internet via the OPNsense
Go to OPNsense and work on the Wizard
Go to the Unbound DNS and check if it is enabled and set it on the LAN only and enable Register ISC DHCP4 Leases
Release the IP on the PC and let it get it again, then do nslookup on the PC name. What will you get?
Enable SSH on the OPNsense and login via putty, then do the command Host followed by the name of your PC
Ping from the SSH to the name of the PC
Check if the DNSSEC is working by using it from your PC the following command: nslookup dnssec-failed.org
Use Override so it resolved example.com as 0.0.0.0

## Slide 2: Blocking ads using DNSBL on OPNsense
Open CNN.com – do you see the advertisements?
Make the configuration needed on OPNsense to block the Domain blocklist big.
Check which are the domains that have been blocked
Go again to CNN.com – do the advertisements open?
Check the report on the DNS – what do you see?
From the report, enable a domain.
From the report, block a domain.

## Slide 3: Unbound DNS as Forwarder on OPNsense
Enable Query Forwarding under Unbound DNS
Reset the IP settings on your PC and check if it has received the right IP assignment
Make from your PC nslookup google.com – is it resolving?
Check the report on the Unbound DNS, what do you see?
Make traffic capture for DNS from Interfaces, Diagnostic, packet capture
Check if CNN.com still has the Ads blocked.
Change DNS on your PC to 8.8.8.8 and then open CNN.com – are the Ads still blocking?

## Slide 4: DNS Forwarder using Dnsmasq on OPNsense
Disable Unbound DNS and check if you can still resolve DNS queries from your PC
Enable DNSmasq using DNS Listen port 53
On DHCP options, set the DNS to be 192.168.1.1
On Domains, set the Domain value to * and IP to be 1.1.1.1 and port 53
Reset the interface card on your PC and check if it has received the right IP assignment
Do nslookup google.com from your PC – is it resolved?
Check the traffic capture as done in the previous LAB
Go to Services → Dnsmasq DNS → Host Overrides and set test.local to 1.2.3.4, then issue nslookup test.local, what do you get?

## Slide 5: CARP Configuration
On R1, set an IP on the opt interface of 172.16.0.1/24 and enable the firewall so all traffic pass on that interface
On R2, set an IP on the opt interface of 172.16.0.2/24 and enable the firewall so all traffic pass on that interface
Ping from one router to another on the opt interface, is it working?
On R1, create a Virtual IP on the LAN with an IP of 192.168.1.254/24, a password 123456, VHID group 1, Advskew 0 and No XMLRPC Sync unchecked (do the same for the WAN).

## Slide 6: DHCP HA Configuration
On R1, ensure that all DHCP servers are disabled (Hint: DNSmasq, ISC, KEA)
Enable KEA Control Agent with bind address 172.16.0.1 and Bind port 8101
Enable KEA DHCPv4 on LAN interface and enable High Availability (Hint: remember the server name)
Add a subnet of 192.168.1.0/24 with pool from 1.100 till 1.200, Gateway and DNS of 192.168.1.254
On HA Peers, create one entry with name OPNsense, role primary and URL 172.16.0.1:8111
On HA Peers, create one entry with name OPNsense2, role secondary and URL 172.16.0.2:8111

## Slide 7: High Availability Configuration
On R1, Go to System, High Availability, set the Synchronize all states via to OPT, Synchronize Peer IP to 172.16.0.2, Synchronize Config to 172.16.0.2:443, uncheck verify peer and put the remote username and password, and finally select all services
Check the status and synchronize everything to R2
Check if R2 has gotten all configuration (CARP and DHCP)

## Slide 8: High Availability Test
Check if your PC got an IP assignment and see how the traffic is going?
Make an extended ping to google.com then remove the cable on the primary router. Is ping still working
Re-put the cable and check how the traffic is flowing now
Ping to google.com and remove the WAN cable. Is the ping still working?
Re-put the WAN, and remove the LAN cable from R1 then try to get an IP to your PC again – is it working?