## Slide 1: Connect your router to 2 ISP’s
Enable DHCP client on Eth1 and on Eth2 then check if you have internet from both interfaces
Put an IP address on Eth3 of 172.16.0.1/24
Check if each link is providing 2M/2M as speed
Configure DHCP Server on R1 on Eth3
Configure NAT so the internet work from both ISP’s
Check on your PC if you can go to the internet from both ISP’s

## Slide 2: PCC Load Balancing – DHCP
Create a prerouting mangle rule with destination address 192.168.25.0/24 and coming from Eth3 then action accept
Create a prerouting mangle rule with destination address 192.168.26.0/24 and coming from Eth3 then action accept
Create a prerouting mangle rule with destination address 172.16.0.0/24 and action accept
Go to Routing then table, and create 2 entries: one via-ISP1 and one via-ISP2
Create a prerouting mangle rule with In. interface Eth3, PCC classifier both addresses, denominator 2, remainder 0 then action mark connection ISP1-Conn
Create a prerouting mangle rule with In. interface Eth3, PCC classifier both addresses, denominator 2, remainder 1 then action mark connection ISP2-Conn
Create a prerouting mangle rule with mark connection ISP1-Conn, action mark-routing via-ISP1
Create a prerouting mangle rule with mark connection ISP2-Conn, action mark-routing via-ISP2
Create a prerouting mangle rule with In. interface Ether1, action mark connection ISP1-Conn
Create a prerouting mangle rule with In. interface Ether2, action mark connection ISP2-Conn
Create an Output mangle rule with mark connection ISP1-Conn, action mark-routing via-ISP1
Create an Output mangle rule with mark connection ISP2-Conn, action mark-routing via-ISP2
Create 2 routes to ISP1 and ISP2 with the mark routing that you have just created
For failover, create a route to ISP1 with the mark via-ISP2 and give it a distance of 2
For failover, create a route to ISP2 with the mark via-ISP1 and give it a distance of 2
Do a test, are you getting 4 Mbps on upload and download?

## Slide 3: PCC Load Balancing with uneven speed – DHCP
Check what speed you have to ISP1 and to ISP2
Make the change needed on the PCC configuration so you can have the full speed
Make a test and check if it is working

## Slide 4: Hotspot installation
Install hotspot on the interface WLAN1
Connect your phone to the hotspot and check if the PCC is working
Disable the 2 default routes received from the ISPs, do you still have internet on your hotspot?

## Slide 5: PCC on Hotspot
On the PCC rules, put in interface WLAN1 and dst address !local, and hotspot Auth
On all rules, change Ethe3 to WLAN1
Connect to the Hotspot from your phone, do you have internet?
Try to do speedtest, what do you get?

## Slide 6: PPPoE server and client
Remove the IP address and the DHCP server from the interface Eth3
Configure a PPPoE pool with range of 192.168.155.2 – 192.168.155.254
From PPP, configure a PPPoE profile with local address 192.168.155.1, remote address the PPPoE pool
Create a secret with username user1 and password user1 and profile the one you created
Configure the PPPoE server to run on Eht3 and to have the default profile of the one you created
Create a PPPoE client on your Windows machine and connect to the PPPoE server of the MikroTik router and check if the PC is connected to the internet

## Slide 7: PCC on PPPoE
Go to interface list and create a list as PPPoE and don’t put any interface in it for now
Go to the PPPoE profile and add interface list the PPPoE list that was created
On the accept rule, instead of putting the IP of Eh3 that was before, put the IP of the PPPoE server
Remove the in interface on the PCC rules and Routing Mark rules, and put instead the in interface list which is PPPoE
Disconnect your PC from PPPoE and reconnect again
Check if you see something inside the interface list on the MikroTik router
Do a test and see if the PCC is working and getting the full speed

## Slide 8: PCC with 2 same gateways
Enable DHCP client on Eht1 and Eth2 and don’t put default route
Set an IP of 172.16.0.1/24 on Eth3 and enable DHCP server
Enable NAT on Eth1 and Eth2 as out interface
Go to IP, VRF and create vrf-ISP1 and put inside of it Eth1, then vrf-ISP2 and put inside of it Eth2
Accept prerouting going to 192.168.1.0/24 with in Eth3, and going to 172.16.0.0/24
Create PCC rule for ISP1 connections and another one for ISP2 connections
Create Routing mark rule for all ISP1 connections to go to vrf-ISP1 and do the same for ISP2 connection to go to vrf-ISP2
Create a default route with gateway 192.168.1.1, VRF-ISP1, interface Eth1 and routing table vrf-ISP1
Create a default route with gateway 192.168.1.1, VRF-ISP2, interface Eth2 and routing table vrf-ISP2
Make a test if it is working, if not fix the problem
Do backup routes and test if everything is working